Embedded Robot Controller
FLASH
SPI
HDMI
left image
HDMI
right image
ERC-1
S/PDIF
S/PDIF
L/R audio out
L/R audio in
SPI
SPI
action byte stream
sensor byte stream
UART
management
microcontroller
embedded components vs. AI accelerator
real time performance vs. flexibility

---
CNN Vision-Language-Action Model
Conv2d()→ ReLU()
Conv2d()
Upsample()
AvgPool2d(), Multinomial()
[14,14,256]
input
frame
[896,896,3]
 IMAGE
ENCODER
[1,1,256]
output
action
prompt
token
[1,1,256]
[14,14,256]
+
ACTION
DECODER
 TEXT
ENCODER
100Hz
zeros(14,14,256)
[14,14,256]
[1,1,256]
[14,14,256]
next
token
 TEXT
DECODER
CONTEXT
PROJECTOR
100Hz

---
BACKUP

---
CNN Language Model
[H,W,E]
V
[E]
prompt
token
 ENCODER
next
token
zeros(H,W,C)
[H,W,C+E]
[E]
[H,W,C]
[H,W,C]
CAT
 DECODER
PROJECTOR
Conv2d()→ ReLU()
Conv2d()
V	50257
E	256
C	512
H,W	8,8
Upsample(), AvgPool2d()
FROZEN

---
CNN Language Model
[H,W,E]
[E]
prompt
token
 ENCODER
next
token
zeros(H,W,C)
[H,W,C+E]
[E]
[H,W,C]
[H,W,C]
CAT
 DECODER
PROJECTOR
Conv2d()→ ReLU()
Conv2d()
V	50257
E	256
C	512
H,W	8,8
Upsample(), AvgPool2d()
FROZEN

---
CNN Language Model
[H,W,E]
[E]
prompt
token
 ENCODER
next
token
zeros(H,W,C)
[E]
[H,W,C]
[H,W,C]
CAT
PROJECTOR
 DECODER
Conv2d()→ ReLU()
Conv2d()
E	256
V	50257
C	256
H,W	14,14
Upsample()
FROZEN

---
CNN Language Model
[H,W,E]
[E]
prompt
token
 ENCODER
next
token
zeros(H,W,C+E)
[H,W,C]
[E]
[H,W,C+E]
[H,W,C+E]
CAT
PROJECTOR
 DECODER
Conv2d()→ ReLU()
Conv2d()
E	256
V	50257
C	256
H,W	14,14
Upsample()
FROZEN

---
CNN Vision-Language Model
caption
[H,W,256]
[256]
prompt
 TEXT ENCODER
image
[896,896,3]
[256]
[H,W,128]
C
spectrogram
[896,896,1]
IMAGE ENCODER
 TEXT DECODER
zeros(H,W,640)
[H,W,640]
[H,W,256]
[H,W,640]
C
CONTEXT MAP
Conv2d()→ ReLU()
Conv2d()
Upsample()→ Conv2d()
H,W	32,32

---
CNN Perception-Language-Action Model
inner caption
[H,W,256]
[256]
prompt
 TEXT ENCODER
[H,W,128]
left eye
[896,896,3]
C
[256]
[H,W,128]
right eye
[896,896,3]
C
[H,W,64]
spectrogram
[896,896,3]
C
 TEXT DECODER
IMAGE ENCODERS
pose
map
zeros(H,W,C)
[H,W,832]
[H,W,256]
[H,W,832]
C
CONTEXT MAP
 POSE DECODER
Conv2d()→ BatchNorm2d()→ ReLU()
Conv2d()
Upsample()→ Conv2d()
H,W	32,32

---
PHASE 1:
CNN Perception-Language-Action model (CNN-PLA), running on GPU
>20fps, <100ms latency, <400W
PHASE 2:
CNN-PLA model running on FPGA
>100fps, <15ms latency, <100W
PHASE 3:
CNN-PLA model running on ASIC at >300fps, <5ms latency, <10W

---
Seated humanoid :
1-DoF spine
2-DoF shoulder
2-DoF neck
6-DoF arms
6-DoF hands
Data collection :
VR teleoperated
spine/shoulder : swivel chair with up/down control
neck : VR gyroscope
arms/hands : TBD
ROBOT
896x896 RGB at 120Hz, left and right eye
896x896 spectrogram at 120Hz, audio and tactile signals
29-DoF target pose at 120Hz
TELEOPERATOR
transcribed verbal commentary at 120 characters/s
synthetically captioned using open source VL model, 1 character/frame

---
CNN Perception-Language-Action Model
inner caption
[H,W,256]
[256]
prompt
 TEXT ENCODER
[H,W,128]
left eye
[896,896,3]
C
[256]
[H,W,128]
right eye
[896,896,3]
C
[H,W,64]
spectrogram
[896,896,3]
C
 TEXT DECODER
IMAGE ENCODERS
pose
map
zeros(H,W,C)
[H,W,832]
[H,W,256]
[H,W,832]
C
CONTEXT MAP
 POSE DECODER
Conv2d()→ BatchNorm2d()→ ReLU()
Conv2d()
Upsample()→ Conv2d()
H,W	32,32

---
CNN Language Model
[H,W,C]
[E]
prompt
token
 ENCODER CNN
next
token
zeros(H,W,C)
[H,W,C]
[E]
[H,W,C]
[H,W,C]
PROJECTOR CNN
 DECODER CNN
Conv2d()→ ReLU()
Conv2d()
E	256
V	50257
C	384
H,W	14,14
Upsample()
AvgPool()

---
Devices
- TE256A	: Token Encoder, vocab_size=256, ASCII
- TD256A	: Token Decoder, vocab_size=256, ASCII
- CP384V	: Context Projector, n_embd=384, VGG
- IE384R	: Image Encoder, n_embd=384, Resnet
- TD

---
alt = lite-base-resnet-xeno
inner voice
[H,W,C]
[C]
prompt
 TEXT ENCODER
[C]
perception
[H,W,C]
[768,768,3]
 TEXT DECODER
IMAGE ENCODER
zeros(H,W,C)
[H,W,C]
pose
[C]
[H,W,C]
 POSE DECODER
CONTEXT PROJECTOR
Conv2d(kernel=3)→ ReLU()
V	256
C	384
H,W	81,81
Conv2d(kernel=1)
Upsample(scale=3)→ Conv2d(kernel=3)→ ReLU()

---
alt2
[H,W,C]
[C]
prompt
token
REPLICATE
next
token
zeros(H,W,C)
[H,W,C]
[C]
[H,W,C]
[H,W,C]
CONTEXT CNN
 DECODER CNN
Conv2d(kernel=3)→ BatchNorm2d()→ ReLU()
V	256
C	384
H,W	81,81
Conv2d(kernel=1)
Upsample()

---
alt1
[H,W,C]
[C]
prompt
token
TEXT ENCODER CNN
next
token
zeros([H,W,C])
[H,W,C]
[H,W,C]
[C]
[H,W,C]
STATE TRAJECTORY CNN
TEXT DECODER CNN
V	256
C	384
H,W	81,81

---
alt1
[C]
[H,W,C]
current token
TEXT ENCODER CNN
zeros([H,W,C])
[H,W,C]
[H,W,C]
[C]
[H,W,C]
next token
TEXT DECODER CNN
CONTEXT TRAJECTORY CNN
V	256
C	384
H,W	81,81

---
alt1
[C]
[H,W,C]
current token
CNN ENCODER
[H,W,C]
[C]
next token
CNN DECODER
[H,W,C]
[H,W,C]
current context
[H,W,C]
next context
CNN PROJECTOR
V	256
C	384
H,W	81,81

---
multimodal alt1
[C]
[H,W,C]
[C]
[H,W,C]
next token
current token
CNN ENCODER
CNN DECODER
[H,W,C]
next context
[768,768,8]
[H,W,C]
current frame
CNN ENCODER
[H,W,C]
[H,W,C]
current context
V	256
C	384
H,W	81,81
CNN PROJECTOR

---
current context
multimodal alt1
[H,W,C]
[768,768,8]
current frame
CNN ENCODER
[C]
[H,W,C]
[C]
[H,W,C]
next token
current token
CNN ENCODER
CNN DECODER
[H,W,C]
next context
np.zeros([H,W,C])
[H,W,C]
[H,W,C]
V	256
C	384
H,W	81,81
CNN ENCODER

---
current context
multimodal alt1
[H,W,C]
[768,768,16]
[H,W,C]
[768,768,16]
next frame
current frame
CNN ENCODER
CNN ENCODER
[C]
[H,W,C]
[C]
[H,W,C]
next token
current token
CNN ENCODER
CNN DECODER
[H,W,C]
next context
np.zeros([H,W,C])
[H,W,C]
[H,W,C]
V	256
C	384
H,W	81,81
CNN ENCODER

---
alt1
H,W,C
C
int
H,W,C
int
C
next token
current token
CNN ENCODER
CNN DECODER
H,W,C
H,W,C
H,W,C
next context
current context
CNN PROJECTOR

---
current
token
next
token
C
H,W,C
H,W,C
int
int
C
CNN ENCODER
CNN DECODER
H,W,C
H,W,C
×
current
context
next
context
γ
(gamma)

---
alt2
C
H,W,C
int
current token
CNN ENCODER
C
int
H,W,2*C
H,W,C
CAT
next token
CNN DECODER
H,W,C
H,W,C
current context
CNN PROJECTOR
H,W,C
next context

---
alt3
H,W,C
int
E
current
token
CNN ENCODER
H,W,2*C
H,W,C
H,W,C
E
int
CAT
next
token
CNN PROJECTOR
CNN DECODER
H,W,C
current
context
H,W,C
next
context

---
C
H,W,C
C
H,W,C
int
H,W,C
int
current
token
next
token
CNN DECODER
CNN ENCODER
CNN PROJECTOR
H,W,C
H,W,C
×
current
context
next
context
γ
gamma

---
current
token
next
token
C
H,W,C
H,W,C
int
int
C
CNN ENCODER
CNN DECODER
H,W,C
H,W,C
current
context
next
context

---
H,W,C
C
int
H,W,C
int
C
next token
current token
CNN ENCODER
CNN DECODER
H,W,C
H,W,C
H,W,C
next context
current context
CNN PROJECTOR

---
next
token
C
H,W,C
current
token
int
H,W,C
H,W,C
int
C
CNN DECODER
CNN ENCODER
CNN PROJECTOR
H,W,C
H,W,C
next
context
current
context

---
int
H,W,C
C
current token
CNN ENCODER
H,W,C
H,W,C
C
H,W,C
int
next token
current context
CNN DECODER
CNN PROJECTOR
H,W,C
next context